## Slide 1: A+ Guide to Hardware, 9th Edition
Chapter 3
All About Motherboards
Notes: 1
A+ Guide to Hardware, 9th Edition
Chapter 3
All About Motherboards

## Slide 2: Objectives
Describe and contrast various types and features of motherboards
Configure a motherboard using BIOS or UEFI firmware
Maintain a motherboard, including updating drivers, flashing UEFI/BIOS, and replacing the CMOS battery
Select, install, and replace a motherboard
Notes: Objectives
Describe and contrast various types and features of motherboards
Configure a motherboard using BIOS or UEFI firmware
Maintain a motherboard, including updating drivers, flashing UEFI/BIOS, and replacing the CMOS battery
Select, install, and replace a motherboard

## Slide 3: Motherboard Types and Features
Motherboard
  Most complicated computer component
  One of the first items to consider when building a computer
Consider the following when purchasing a motherboard:
  Form factor
  Processor socket and chipset
  Buses and number of bus slots
  Other connectors, slots, and ports
Notes: Motherboard Types and Features
Motherboard
  Most complicated computer component
  One of the first items to consider when building a computer
Consider the following when purchasing a motherboard:
  Form factor
  Processor socket and chipset
  Buses and number of bus slots
  Other connectors, slots, and ports

## Slide 4: Motherboard Form Factors
Determines motherboard size, features
  Compatible with power supplies, cases, processors, expansion cards
Most popular
  ATX, MicroATX, and Mini-ITX(scarce)
    Mini-ITX is smaller than MicroATX and is also known as ITX
The following slides show examples of form factors and comparisons of sizes and hold positions of several form factors
Notes: Motherboard Form Factors
Determines motherboard size, features
  Compatible with power supplies, cases, processors, expansion cards
Most popular
  ATX, MicroATX, and Mini-ITX
    Mini-ITX is smaller than MicroATX and is also known as ITX
The following slides show examples of form factors and comparisons of sizes and hold positions of several form factors

## Slide 5: Motherboard Form Factors
Figure 3-3 A Mini-ITX motherboard
Notes: Motherboard Form Factors

## Slide 6: Motherboard Form Factors
Table 3-1 Motherboard form factors
Notes: Motherboard Form Factors

## Slide 7: Processor Sockets
Processor socket – determines which processors a board can support
  Socket holds Intel or AMD processors
Sockets for Intel processors
  Intel makes several type of processors
Notes: Processor Sockets
Processor socket – determines which processors a board can support
  Socket holds Intel or AMD processors
Sockets for Intel processors
  Intel makes several Itanium and Xeon processors designed for servers

## Slide 8: Processor Sockets
These processors and their corresponding sockets use different methods to make contacts between them:
  Pin grid array (PGA) socket
    Pins aligned in uniform rows around socket
  Land grid array (LGA)
    Uses lands (pads) rather than pins
    Examples of LGA sockets: LGA775 and LGA1366
  Flip-chip land grid array (FCLGA) socket
    Chip is flipped over so that the top of the chip is on the bottom and makes contact with the socket
Notes: Processor Sockets
Sockets and processor use different methods to make contacts between them:
  Pin grid array (PGA) socket
    Pins aligned in uniform rows around socket
  Land grid array (LGA)
    Uses lands (pads) rather than pins
    Examples of LGA sockets: LGA775 and LGA1366
  Flip-chip land grid array (FCLGA) socket
    Chip is flipped over so that the top of the chip is on the bottom and makes contact with the socket

## Slide 9: Processor Sockets
Sockets and processor use different methods to make contacts between them (cont’d):
  Staggered pin grid array (SPGA)
    Pins staggered over socket
    Squeezes more pins into a small space
  Ball grid array (BGA)
    Not really a socket
    Processor is soldered to the motherboard
Notes: Processor Sockets
Sockets and processor use different methods to make contacts between them (cont’d):
  Staggered pin grid array (SPGA)
    Pins staggered over socket
    Squeezes more pins into a small space
  Ball grid array (BGA)
    Not really a socket
    Processor is soldered to the motherboard

## Slide 10: Processor Sockets
Figure 3-7 Socket LGA775 is the first Intel socket to use lands rather than pins
Notes: Processor Sockets

## Slide 11: Processor Sockets
Notes: Processor Sockets

## Slide 12: Processor Sockets
Zero insertion force (ZIF) sockets
  All current processor sockets
  Side lever lifts processor up and out of the socket
Sockets for AMD Processors
  AMD uses the PGA socket architecture (desktops)
Notes: Processor Sockets
Zero insertion force (ZIF) sockets
  All current processor sockets
  Side lever lifts processor up and out of the socket
Sockets for AMD Processors
  AMD uses the PGA socket architecture (desktops)

## Slide 13: Processor Sockets
Table 3-3 Sockets for AMD processors used for desktop computers
Notes: Processor Sockets

## Slide 14: Processor Sockets
Match a processor to the socket and motherboard
  Refer to motherboard, processor compatibility documentation
Figure 3-10 AMD Athlon 64 processor to be inserted into an AM2+ socket
Notes: Processor Sockets
Match a processor to the socket and motherboard
  Refer to motherboard, processor compatibility documentation

## Slide 15: The Chipset
Chipset: set of chips on motherboard that work with processor to collectively control:
  Memory, motherboard buses, some peripherals
Major manufacturers
  Intel and AMD
Intel Chipsets(N/S bridge, Nehalem, Sandy bridge, Ivy bridge, Haswell and Broadwell, …)
  North Bridge and South Bridge - Uses hub interface
    All I/O buses (input/output buses) connect to hub
      Hub connects to system bus
    North Bridge – fast end of hub
    South Bridge – slow end of hub
Notes: The Chipset
Chipset: set of chips on motherboard that work with processor to collectively control:
  Memory, motherboard buses, some peripherals
Major manufacturers
  Intel and AMD
Intel Chipsets
  North Bridge and South Bridge - Uses hub interface
    All I/O buses (input/output buses) connect to hub
      Hub connects to system bus
    North Bridge – fast end of hub
    South Bridge – slow end of hub

## Slide 16: The Chipset
Figure 3-11 The chipset’s North Bridge and South Bridge control access to the
processor for all components
Notes: The Chipset

## Slide 17: The Chipset
Intel Chipsets (cont’d)
  Nehalem chipset
    Contain memory controller within processor housing
    Memory connects directly to processor
    Has QuickPath Interconnect (QPI) technology
      Has 16 lanes for data packets
  Sandy Bridge chipset
    Memory and graphics controller in processor
    Second Generation Core i7 processor is an example
    Sandy Bridge motherboards use DDR3 memory
Notes: The Chipset
Intel Chipsets (cont’d)
  Nehalem chipset
    Contain memory controller within processor housing
    Memory connects directly to processor
    Has QuickPath Interconnect (QPI) technology
      Has 16 lanes for data packets
  Sandy Bridge chipset
    Memory and graphics controller in processor
    Second Generation Core i7 processor is an example
    Sandy Bridge motherboards use DDR3 memory

## Slide 18: The Chipset
Figure 3-12 X58 chipset architecture
Notes: The Chipset
Intel Chipsets (cont’d)
  Nehalem chipset
    Contain memory controller within processor housing
    Memory connects directly to processor
    Has QuickPath Interconnect (QPI) technology
      Has 16 lanes for data packets
  Sandy Bridge chipset
    Memory and graphics controller in processor
    Second Generation Core i7 processor is an example
    Sandy Bridge motherboards use DDR3 memory

## Slide 19: The Chipset
Intel Chipsets (cont’d)
  Ivy Bridge chipset – 3rd generation processors released in 2012
    Use less power
    More transistors in a smaller place
    Perform better than earlier products
    Uses a single Platform Controller Hub
Notes: The Chipset
Intel Chipsets (cont’d)
  Ivy Bridge chipset – 3rd generation processors released in 2012
    Use less power
    More transistors in a smaller place
    Perform better than earlier products
    Uses a single Platform Controller Hub

## Slide 20: The Chipset
Intel Chipsets (cont’d)
  Haswell and Broadwell chipsets
    Haswell - released in 2013
      Work with the LGA1150 and LGA2011 sockets
      Work with DDR3 and DDR4 memory and use less power than previous chipsets
    Broadwell – released in 2015
      Faster than the Haswell chipsets
      Use the LGA1150 socket
Notes: The Chipset
Intel Chipsets (cont’d)
  Haswell and Broadwell chipsets
    Haswell - released in 2013
      Work with the LGA1150 and LGA2011 sockets
      Work with DDR3 and DDR4 memory and use less power than previous chipsets
    Broadwell – released in 2015
      Faster than the Haswell chipsets
      Use the LGA1150 socket

## Slide 21: The Chipset
AMD chipsets
  AMD A-series
    Designed to support the AMD Accelerated Processing Unit (APU), which is a combination of a CPU and a graphics processing unit (GPU)
    Support AMD CrossFire technology, which uses dual video cards in the same system
  AMD 9-series
    Designed to support AMD processors that can have up to eight cores
Notes: The Chipset
AMD chipsets
  AMD A-series
    Designed to support the AMD Accelerated Processing Unit (APU), which is a combination of a CPU and a graphics processing unit (GPU)
    Support AMD CrossFire technology, which uses dual video cards in the same system
  AMD 9-series
    Designed to support AMD processors that can have up to eight cores

## Slide 22: Buses and Expansion Slots
Bus
  System of pathways used for communication
Carried by bus:
  Power, control signals, memory addresses, data
  These lines are sometimes called data bus
Data and instructions exist in binary
  Only two states: on and off
Data path size: width of a data bus
  Examples: 8-bit bus has eight wire (lines) to transmit
Notes: Buses and Expansion Slots
Bus
  System of pathways used for communication
Carried by bus:
  Power, control signals, memory addresses, data
  These lines are sometimes called data bus
Data and instructions exist in binary
  Only two states: on and off
Data path size: width of a data bus
  Examples: 8-bit bus has eight wire (lines) to transmit

## Slide 23: Buses and Expansion Slots
Figure 3-17 A data bus has traces or lines that carry voltage interpreted
by the CPU and other devices as bits
Notes: Buses and Expansion Slots

## Slide 24: Buses and Expansion Slots
System clock (system timer) – times activities on the motherboard
Speed of memory, Front Side Bus, processor, or other component is measured in hertz (Hz), which is one cycle per second
  Megahertz (MHz): one million cycles per second
  Gigahertz (GHz): one billion cycles per second
Motherboards can have more than one bus
  Table 3-4 on the following slide lists many buses
Notes: Buses and Expansion Slots
System clock (system timer) – times activities on the motherboard
Speed of memory, Front Side Bus, processor, or other component is measured in hertz (Hz), which is one cycle per second
  Megahertz (MHz): one million cycles per second
  Gigahertz (GHz): one billion cycles per second
Motherboards can have more than one bus
  Table 3-4 on the following slide lists many buses

## Slide 25: Buses and Expansion Slots
Table 3-4 Buses listed by throughput
Notes: Buses and Expansion Slots

## Slide 26: Buses and Expansion Slots
Conventional PCI(Peripheral Component Interconnect, a local bus standard developed by Intel Corporation. Most modern PCs include a PCI bus in addition to a more general ISA expansion bus).
  Improved several times
  PCI Version 2.x introduced the 64-bit, 3.3 V PCI slot, doubling the data throughput of the bus
  Four types of slots and six possible
  PCI card configurations
Notes: Buses and Expansion Slots
Conventional PCI
  Improved several times
  PCI Version 2.x introduced the 64-bit, 3.3 V PCI slot, doubling the data throughput of the bus
  Four types of slots and six possible PCI card configurations

## Slide 27: Buses and Expansion Slots
PCI-X
  Uses 64-bit data path
  Latest revision is PCI-X 3.0 (all revisions are backward-compatible)
Figure 3-20 The two long white
PCI-X slots can support PCI cards
Notes: Buses and Expansion Slots
PCI-X
  Uses 64-bit data path
  Latest revision is PCI-X 3.0 (all revisions are backward-compatible)

## Slide 28: Buses and Expansion Slots
PCI Express (PCIe)
  Not backward compatible with conventional PCI or PCI-X
  Expected to replace both PCI and PCI-X
  Uses a serial bus, which is faster than parallel
  Comes in four different slot sizes
    PCI Express x1, x4, x8, and x16
  Latest version is PCIe 4.0 which doubles the throughput of version 3.0
Notes: Buses and Expansion Slots
PCI Express (PCIe)
  Not backward compatible with conventional PCI or PCI-X
  Expected to replace both PCI and PCI-X
  Uses a serial bus, which is faster than parallel
  Comes in four different slot sizes
    PCI Express x1, x4, x8, and x16
  Latest version is PCIe 4.0 which doubles the throughput of version 3.0

## Slide 29: Buses and Expansion Slots
Figure 3-21 Three types of PCIe slots and one conventional PCI slot
Notes: Buses and Expansion Slots

## Slide 30: Buses and Expansion Slots
MiniPCi and MiniPCIe in Laptops
  Smaller versions of the PCI and PCIe slots
  Mini PCIe slots have 52 or 54 pins and one notch offset from the center of the slot
  Mini PCI slot is wider with 100 or 124 pins
Figure 3-23 Mini PCIe slot with a wireless Mini PCIe card installed
Notes: Buses and Expansion Slots
MiniPCi and MiniPCIe in Laptops
  Smaller versions of the PCI and PCIe slots
  Mini PCIe slots have 52 or 54 pins and one notch offset from the center of the slot
  Mini PCI slot is wider with 100 or 124 pins

## Slide 31: Buses and Expansion Slots
PCI Riser cards
  Installs in a PCI slot and provides another slot at a right angle
  Used to fit PCI, PCIe, and PCI-X cards into a low-profile or slimline case
Figure 3-25 PCI riser card provides a 3.3-V slot or 5-V slot depending on which direction the card is inserted in the PCI slot
Notes: Buses and Expansion Slots
PCI Riser cards
  Installs in a PCI slot and provides another slot at a right angle
  Used to fit PCI, PCIe, and PCI-X cards into a low-profile or slimline case

## Slide 32: Onboard Ports and Connectors
Onboard ports (integrated components)
  Ports coming directly off the motherboard
    USB, sound, network, FireWire, video, eSATA ports
    Older motherboards might have mouse and keyboard ports, parallel and serial ports
I/O shield
  Plate installed in computer case providing holes for on-board ports
Internal connectors
  SATA, USB or FireWire (IEEE 1394) connectors
Notes: Onboard Ports and Connectors
Onboard ports (integrated components)
  Ports coming directly off the motherboard
    USB, sound, network, FireWire, video, eSATA ports
    Older motherboards might have mouse and keyboard ports, parallel and serial ports
I/O shield
  Plate installed in computer case providing holes for on-board ports
Internal connectors
  SATA, USB or FireWire (IEEE 1394) connectors

## Slide 33: Onboard Ports and Connectors
Notes: Onboard Ports and Connectors
Onboard ports (integrated components)
  Ports coming directly off the motherboard
    USB, sound, network, FireWire, video, eSATA ports
    Older motherboards might have mouse and keyboard ports, parallel and serial ports
I/O shield
  Plate installed in computer case providing holes for on-board ports
Internal connectors
  SATA, USB or FireWire (IEEE 1394) connectors

## Slide 34: Configuring a Motherboard
Firmware is used to configure a motherboard
Motherboard settings
  Enable or disable connector or port
  Set CPU frequency, system bus, other buses
  Control security features
  Control what happens when PC first boots
Motherboards may use these types of firmware:
  BIOS – used on older motherboards
  UEFI – replacing BIOS
  UEFI with BIOS – for backward compatibility
Notes: Configuring a Motherboard
Motherboard settings
  Enable or disable connector or port
  Set CPU frequency, system bus, other buses
  Control security features
  Control what happens when PC first boots
Motherboards may use these types of firmware:
  BIOS – used on older motherboards
  UEFI – replacing BIOS
  UEFI with BIOS – for backward compatibility

## Slide 35: Using BIOS Setup To Configure a Motherboard
Access the BIOS Setup Program
  Press a key or combination of keys during the boot process
    Varies from one manufacturer to another
    See documentation for your motherboard or watch the screen near the beginning of the boot
  Setup screen appears with menus and Help features
Notes: Using BIOS Setup To Configure a Motherboard
Access the BIOS Setup Program
  Press a key or combination of keys during the boot process
    Varies from one manufacturer to another
    See documentation for your motherboard or watch the screen near the beginning of the boot
  Setup screen appears with menus and Help features

## Slide 36: Using BIOS Setup To Configure a Motherboard
Figure 3-31 BIOS setup main menu
Notes: Using BIOS Setup To Configure a Motherboard

## Slide 37: Using Setup BIOS To Configure a Motherboard
Change the boot sequence
  Might need to change boot sequence from hard drive to DVD for a new Windows install
  After the OS is installed, change setup BIOS to boot first from the hard drive
    To prevent accidental boots from a DVD or other media
  If troubleshooting a boot problem, be sure to set BIOS to perform a full POST
Notes: Using Setup BIOS To Configure a Motherboard
Change the boot sequence
  Might need to change boot sequence from hard drive to DVD for a new Windows install
  After the OS is installed, change setup BIOS to boot first from the hard drive
    To prevent accidental boots from a DVD or other media
  If troubleshooting a boot problem, be sure to set BIOS to perform a full POST

## Slide 38: Using Setup BIOS To Configure a Motherboard
Configure onboard devices
  Enable/disable a port or group of ports
View hard drive and optical drive information
Processor and clock speeds
  Some motherboards allow changing the processor speed and/or the memory multiplier (overclocking)
Monitor temperatures, fan speeds, and voltages
Intrusion detection
  Can enable event logging (logs when case is opened)
Notes: Using Setup BIOS To Configure a Motherboard
Configure onboard devices
  Enable/disable a port or group of ports
View hard drive and optical drive information
Processor and clock speeds
  Some motherboards allow changing the processor speed and/or the memory multiplier (overclocking)
Monitor temperatures, fan speeds, and voltages
Intrusion detection
  Can enable event logging (logs when case is opened)

## Slide 39: Using Setup BIOS To Configure a Motherboard
Power-on passwords
  Assigned in BIOS setup to prevent unauthorized access to the computer and/or BIOS setup utility
  May be possible to set a supervisor and user password
    If both passwords are set, must enter a valid password to boot the system
  How to set passwords varies depending on motherboard and BIOS
Notes: Using Setup BIOS To Configure a Motherboard
Power-on passwords
  Assigned in BIOS setup to prevent unauthorized access to the computer and/or BIOS setup utility
  May be possible to set a supervisor and user password
    If both passwords are set, must enter a valid password to boot the system
  How to set passwords varies depending on motherboard and BIOS

## Slide 40: Using Setup BIOS To Configure a Motherboard
BIOS Support for Virtualization
  Virtualization is when one physical machine hosts activities that are normally done on multiple machines
  Virtual machine (VM) is software that simulates the hardware of a physical computer
    Each VM works like a physical computer and is assigned virtual devices such as virtual motherboard and virtual hard drive
  Virtualization must be enabled in BIOS setup
Notes: Using Setup BIOS To Configure a Motherboard
BIOS Support for Virtualization
  Virtualization is when one physical machine hosts activities that are normally done on multiple machines
  Virtual machine (VM) is software that simulates the hardware of a physical computer
    Each VM works like a physical computer and is assigned virtual devices such as virtual motherboard and virtual hard drive
  Virtualization must be enabled in BIOS setup

## Slide 41: Using Setup BIOS To Configure a Motherboard
LoJack for Laptops Technology
  Technology embedded in the BIOS of many laptops to protect a system against theft
  Must subscribe to service
  Software and BIOS work together to locate a laptop whenever it connects to the Internet
Drive Encryption and Drive Password Protection
  Some motherboards allow you to set a password in order to access the hard drive
  Password is kept on drive so that it still works even if drive is moved to another computer
Notes: Using Setup BIOS To Configure a Motherboard
LoJack for Laptops Technology
  Technology embedded in the BIOS of many laptops to protect a system against theft
  Must subscribe to service
  Software and BIOS work together to locate a laptop whenever it connects to the Internet
Drive Encryption and Drive Password Protection
  Some motherboards allow you to set a password in order to access the hard drive
  Password is kept on drive so that it still works even if drive is moved to another computer

## Slide 42: Using Setup BIOS To Configure a Motherboard
Exiting the BIOS setup menus
  Most exit screens give several options
Figure 3-40 BIOS setup Exit menu
Notes: Using Setup BIOS To Configure a Motherboard
Exiting the BIOS setup menus
  Most exit screens give several options

## Slide 43: Using UEFI Setup to Configure a Motherboard
Extensible Firmware Interface (EFI), original version first developed by Intel
Improves on BIOS in these ways:
  Faster and better booting
  Mouse-enabled interface
  Secure boot
  Support for hard drives larger than 2 TB
Provides a BIOS boot through its Compatibility Support Module (CSM)
Notes: Using UEFI Setup to Configure a Motherboard
Extensible Firmware Interface (EFI), original version first developed by Intel
Improves on BIOS in these ways:
  Faster and better booting
  Mouse-enabled interface
  Secure boot
  Support for hard drives larger than 2 TB
Provides a BIOS boot through its Compatibility Support Module (CSM)

## Slide 44: Maintaining a Motherboard
Motherboard is considered a field replaceable unit
  Need to know how to:
    Update motherboard drivers
    Flash BIOS or UEFI
    Replace CMOS battery
Notes: Maintaining a Motherboard
Motherboard is considered a field replaceable unit
  Need to know how to:
    Update motherboard drivers
    Update flash BIOS or UEFI
    Replace CMOS battery

## Slide 45: Updating Motherboard Drivers
Device drivers are small programs that allow software to interact with certain hardware
Use Windows internal drivers, bundled CD drivers, or download drivers from manufacturer site
Always use 32-bit drivers with a 32-bit OS and 64-bit drivers with a 64-bit OS
Notes: Updating Motherboard Drivers
Device drivers are small programs that allow software to interact with certain hardware
Use Windows internal drivers, bundled CD drivers, or download drivers from manufacturer site
Always use 32-bit drivers with a 32-bit OS and 64-bit drivers with a 64-bit OS

## Slide 46: Flashing BIOS
Flashing BIOS is the process of upgrading or refreshing the programming stored on the firmware chip
  BIOS updates are downloaded from motherboard manufacturer’s Web site or third party site
  Performed if:
    System hangs at odd times or during boot
    Motherboard becomes unstable
    Incorporating new feature, or component
Notes: Flashing BIOS
Flashing BIOS is the process of upgrading or refreshing the programming stored on the firmware chip
  BIOS updates are downloaded from motherboard manufacturer’s Web site or third party site
  Performed if:
    System hangs at odd times or during boot
    Motherboard becomes unstable
    Incorporating new feature, or component

## Slide 47: Flashing BIOS
Methods of installing BIOS updates
  Express BIOS update
  Update from a USB flash drive using setup BIOS
  Update using a bootable CD
  Recovery from a failed update
“If it’s not broke, don’t fix it” – only update if you’re having trouble with a motherboard
Don’t update unless the update is a later version than the one installed
Update should not be interrupted while in progress
Notes: Flashing BIOS
Methods of installing BIOS updates
  Express BIOS update
  Update from a USB flash drive using setup BIOS
  Update using a bootable CD
  Recovery from a failed update
“If it’s not broke, don’t fix it” – only update if you’re having trouble with a motherboard
Don’t update unless the update is a later version than the one installed
Update should not be interrupted while in progress

## Slide 48: Flashing UEFI
UEFI updates are more secure than BIOS updates
  Require digital signatures for update to be verified
UEFI firmware, drivers, and databases can be updated by way of a USB flash drive or from within Windows
Windows updates sometimes include UEFI updates
  When Windows receives a UEFI update, it hands off the update to UEFI
  Firmware is responsible for applying the update and displays a screen letting user know not to disturb the system while the update is in progress
Notes: Flashing UEFI
UEFI updates are more secure than BIOS updates
  Require digital signatures for update to be verified
UEFI firmware, drivers, and databases can be updated by way of a USB flash drive or from within Windows
Windows updates sometimes include UEFI updates
  When Windows receives a UEFI update, it hands off the update to UEFI
  Firmware is responsible for applying the update and displays a screen letting user know not to disturb the system while the update is in progress

## Slide 49: Using Jumpers to Clear BIOS Settings
Jumper – two small posts or metal pins that stick up off the motherboard that is open or closed
  Open jumper has no cover and a closed jumper has a cover on the two pins
Jumpers can be used to clear a forgotten supervisor or power-on password
If flashing BIOS fails, a jumper can
be set to undo the update
Notes: Using Jumpers to Clear BIOS Settings
Jumper – two small posts or metal pins that stick up off the motherboard that is open or closed
  Open jumper has no cover and a closed jumper has a cover on the two pins
Jumpers can be used to clear a forgotten supervisor or power-on password
If flashing BIOS fails, a jumper can be set to undo the update

## Slide 50: Replacing the CMOS Battery
CMOS (complementary metal-oxide semiconductor) RAM is a small amount of memory stored on the motherboard that retains data
  Even when computer is turned off
  If the CMOS battery is disconnected or fails, setup information is lost
Notes: Replacing the CMOS Battery
CMOS (complementary metal-oxide semiconductor) RAM is a small amount of memory stored on the motherboard that retains data
  Even when computer is turned off
  If the CMOS battery is disconnected or fails, setup information is lost
To replace the CMOS battery:
  Choose correct replacement battery
  Power down system, unplug it, press power button to drain the power, remove case cover
  Use ESD strap, remove old battery using a flat-head screwdriver, pop new battery into place

## Slide 51: Replacing the CMOS Battery
To replace the CMOS battery:
  Choose correct replacement battery
  Power down system, unplug it, press power button to drain the power, remove case cover
  Use ESD strap, remove old battery using a flat-head screwdriver, pop new battery into place
Notes: Replacing the CMOS Battery
CMOS (complementary metal-oxide semiconductor) RAM is a small amount of memory stored on the motherboard that retains data
  Even when computer is turned off
  If the CMOS battery is disconnected or fails, setup information is lost
To replace the CMOS battery:
  Choose correct replacement battery
  Power down system, unplug it, press power button to drain the power, remove case cover
  Use ESD strap, remove old battery using a flat-head screwdriver, pop new battery into place

## Slide 52: Installing or Replacing a Motherboard
A motherboard is considered a field replaceable unit
A technician needs to know how to:
  Select an appropriate motherboard
  Install or replace one in a desktop or laptop computer
Notes: Installing or Replacing a Motherboard
A motherboard is considered a field replaceable unit
A technician needs to know how to:
  Select an appropriate motherboard
  Install or replace one in a desktop or laptop computer

## Slide 53: How to Select a Desktop Motherboard
Three approaches to selecting a motherboard:
  Select the board that provides the most room for expansion, so you can upgrade and exchange components and add devices easily
  Select the board that best suits the needs of the computer’s current configuration
  Select a motherboard that meets your present needs with moderate room for expansion
Notes: How to Select a Desktop Motherboard
Three approaches to selecting a motherboard:
  Select the board that provides the most room for expansion, so you can upgrade and exchange components and add devices easily
  Select the board that best suits the needs of the computer’s current configuration
  Select a motherboard that meets your present needs with moderate room for expansion

## Slide 54: How to Select a Desktop Motherboard
Consider the following when selecting a motherboard:
  Form factor
  The brand (Intel or AMD) and model processors the board supports
  Chipset and memory speeds the board supports
  Expansion slots (type and how many needed)
  Hard drive controllers
  Case
  Price and warranty
  Support
Notes: How to Select a Desktop Motherboard
Consider the following when selecting a motherboard:
  Form factor
  The brand (Intel or AMD) and model processors the board supports
  Chipset and memory speeds the board supports
  Expansion slots (type and how many needed)
  Hard drive controllers
  Case
  Price and warranty
  Support

## Slide 55: How to Install or Replace a Motherboard
General process for replacing a motherboard:
  1. Verify right motherboard is selected
  2. Get familiar with documentation, features, settings
  3. Remove components to reach old motherboard
  4. Install the I/O shield (metal plate)
  5. Install motherboard
  6. Install processor and processor cooler
  7. Install RAM
  8. Attach cabling (case switches, power supply, drives)
Notes: How to Install or Replace a Motherboard
General process for replacing a motherboard:
  1. Verify right motherboard is selected
  2. Get familiar with documentation, features, settings
  3. Remove components to reach old motherboard
  4. Install the I/O shield (metal plate)
  5. Install motherboard
  6. Install processor and processor cooler
  7. Install RAM
  8. Attach cabling (case switches, power supply, drives)

## Slide 56: How to Install or Replace a Motherboard
General process for replacing motherboard (cont’d.)
  9. Install video card on motherboard
  10. Plug in PC, attach monitor, keyboard
  11. Boot system, enter UEFI/BIOS setup
  12. Observe POST, verify no errors
  13. Verify Windows starts with no errors
  14. Install the motherboard drivers
  15. Install other expansion cards and drivers
  16. Verify system operating properly, make final OS and UEFI/BIOS adjustments
    setting power-on passwords
Notes: How to Install or Replace a Motherboard
General process for replacing motherboard (cont’d.)
  9. Install video card on motherboard
  10. Plug in PC, attach monitor, keyboard
  11. Boot system, enter UEFI/BIOS setup
  12. Observe POST, verify no errors
  13. Verify Windows starts with no errors
  14. Install the motherboard drivers
  15. Install other expansion cards and drivers
  16. Verify system operating properly, make final OS and UEFI/BIOS adjustments
    setting power-on passwords

## Slide 57: Replacing a Laptop System Board
May need to fully disassemble the entire notebook
  Consider alternatives before proceeding
General procedure for replacing the motherboard:
  Remove the keyboard, optical drive, and mini PCIe card
  Remove the notebook lid and keyboard bezel assembly
  Lift up the assembly and disconnect two cables connecting it to the motherboard
  Remove CPU and DVD drive
  Remove screw that hold motherboard in place
Notes: Replacing a Laptop System Board
May need to fully disassemble the entire notebook
  Consider alternatives before proceeding
General procedure for replacing the motherboard:
  Remove the keyboard, optical drive, and mini PCIe card
  Remove the notebook lid and keyboard bezel assembly
  Lift up the assembly and disconnect two cables connecting it to the motherboard
  Remove CPU and DVD drive
  Remove screw that hold motherboard in place

## Slide 58: Summary
The motherboard is the most complicated of all components inside a computer
Most popular motherboard form factors are ATX, MicroATX and Mini-ITX
Motherboard will have one or more processor sockets
Chipset embedded on the motherboard determines what kind of processor/memory are supported
Major advancements in Intel: Accelerated Hub Architecture, Nehalem chipsets, and Sandy Bridge
Notes: Summary
The motherboard is the most complicated of all components inside a computer
Most popular motherboard form factors are ATX, MicroATX and Mini-ITX
Motherboard will have one or more processor sockets
Chipset embedded on the motherboard determines what kind of processor/memory are supported
Major advancements in Intel: Accelerated Hub Architecture, Nehalem chipsets, and Sandy Bridge

## Slide 59: Summary
Buses include conventional PCI, PIC-X, and PCI Express
Some components can be built into the motherboard, called on-board components
Firmware that controls a motherboard and the boot is the older BIOS and the newer UEFI
Settings that can be changed include: changing boot order, enabling or disabling onboard devices, support for virtualization, and security settings
Notes: Summary
Buses include conventional PCI, PIC-X, and PCI Express
Some components can be built into the motherboard, called on-board components
Firmware that controls a motherboard and the boot is the older BIOS and the newer UEFI
Settings that can be changed include: changing boot order, enabling or disabling onboard devices, support for virtualization, and security settings

## Slide 60: Summary
Motherboard drivers and/or BIOS might need updating to fix a problem
CMOS battery might need replacing
When selecting a motherboard pay attention to the form factor, chipset, expansion slots, memory slots, and processors supported
Study motherboard manual before installing it
For laptops, it’s usually more cost effective to replace the laptop than to replace a failed system board
Notes: Summary
Motherboard drivers and/or BIOS might need updating to fix a problem
CMOS battery might need replacing
When selecting a motherboard pay attention to the form factor, chipset, expansion slots, memory slots, and processors supported
Study motherboard manual before installing it
For laptops, it’s usually more cost effective to replace the laptop than to replace a failed system board