## Slide 1: A+ Guide to Hardware, 9th Edition
Chapter 4
Supporting Processors and Upgrading Memory
Notes: A+ Guide to Hardware, 9th Edition
Chapter 4
Supporting Processors and Upgrading Memory

## Slide 2: Objectives
Compare characteristics and purposes of Intel and AMD processors used for personal computers
Install and upgrade a processor
Compare the different kinds of physical memory and how they work
Upgrade memory
Notes: Objectives
Compare characteristics and purposes of Intel and AMD processors used for personal computers
Install and upgrade a processor
Compare the different kinds of physical memory and how they work
Upgrade memory

## Slide 3: Types and Characteristics of Processors
Processor
  Installed on motherboard
  Determines system computing power
Two major processor manufacturers
  Intel and AMD
Figure 4-1 An AMD Athlon 64 X2 installed in socket AM2+ with cooler not yet installed
Notes: Types and Characteristics of Processors
Processor
  Installed on motherboard
  Determines system computing power
Two major processor manufacturers
  Intel and AMD

## Slide 4: Types and Characteristics of Processors
Features affecting processor performance and compatibility with motherboards
  Processor speed
  Socket and chipset the processor can use
  Processor architecture
  Multiprocessing abilities
    Multiprocessing
    Multithreading
    Multicore processing
    Dual processor
Notes: Types and Characteristics of Processors
Features affecting processor performance and compatibility with motherboards
  Processor speed
  Socket and chipset the processor can use
  Processor architecture
  Multiprocessing abilities
    Multiprocessing
    Multithreading
    Multicore processing
    Dual processor

## Slide 5: Types and Characteristics of Processors
Features affecting processor performance and compatibility with motherboards (cont’d)
  Memory cache
  Security
  Memory features on the motherboard that the processor can support
  Support for virtualization
  Integrated graphics
Notes: Types and Characteristics of Processors
Features affecting processor performance and compatibility with motherboards (cont’d)
  Memory cache
  Security
  Memory features on the motherboard that the processor can support
  Support for virtualization
  Integrated graphics

## Slide 6: How a Processor Works
Basic components
  Input/output (I/O) unit
    Manages data and instructions entering and leaving the processor
  Control unit
    Manages all activities inside the processor
  One or more arithmetic logic units (ALUs)
    Performs all logical comparisons, calculations
Notes: How a Processor Works
Basic components
  Input/output (I/O) unit
    Manages data and instructions entering and leaving the processor
  Control unit
    Manages all activities inside the processor
  One or more arithmetic logic units (ALUs)
    Performs all logical comparisons, calculations

## Slide 7: How a Processor Works
Basic components (cont’d)
  Registers
    Small holding areas on processor chip
    Holds counters, data, instructions, and addresses that the ALU is currently processing
  Internal memory caches (L1, L2, L3)
    Holds data and instructions to be processed by ALU
  Buses
    Connect components within the processor housing
Notes: How a Processor Works
Basic components (cont’d)
  Registers
    Small holding areas on processor chip
    Holds counters, data, instructions, and addresses ALU is currently processing
  Internal memory caches (L1, L2, L3)
    Holds data and instructions to be processed by ALU
  Buses
    Connect components within the processor housing

## Slide 8: How a Processor Works
Figure 4-5 Since the Pentium processor was first released in 1993, the standard has been
for a processor to have two arithmetic logic units so that it can process
two instructions at once
Notes: How a Processor Works

## Slide 9: How a Processor Works
Processor frequency (speed)
  Speed at which processor operates internally
Multiplier
  Factor multiplied against system bus frequency
    Determines processor frequency
  System bus frequency × multiplier = processor frequency
Processors sold today contain ALUs and registers that can process 32 bits or 64 bits at a time
Notes: How a Processor Works
Processor frequency (speed)
  Speed at which processor operates internally
Multiplier
  Factor multiplied against system bus frequency
    Determines processor frequency
  System bus frequency × multiplier = processor frequency
Processors sold today contain ALUs and registers that can process 32 bits or 64 bits at a time

## Slide 10: How a Processor Works
Three categories of processors:
  32-bit processors – known as x86 processors
    Can handle 32-bit instructions from OS
  Hybrid processors – known as x86-64 processors
    Can handle a 32-bit OS or a 64-bit OS
    AMD produced the first one (called AMD64)
  64-bit processors – known as x64 processors or IA64
    Require a 64-bit OS and can handle 32-bit applications only by simulating 32-bit processing
Notes: How a Processor Works
Three categories of processors:
  32-bit processors – known as x86 processors
    Can handle 32-bit instructions from OS
  Hybrid processors – known as x86-64 processors
    Can handle a 32-bit OS or a 64-bit OS
    AMD produced the first one (called AMD64)
  64-bit processors – known as x64 processors or IA64
    Require a 64-bit OS and can handle 32-bit applications only by simulating 32-bit processing

## Slide 11: How a Processor Works
Memory cache (L1, L2, or L3)
  Each core in a processor has its own L1 and L2 caches
  All cores might share an L3 cache within the processor package
  Improves performance
Memory controller
  Included in processor package
  Significant increase in system performance
Notes: How a Processor Works
Memory cache (L1, L2, or L3)
  Each core in a processor has its own L1 and L2 caches
  All cores might share an L3 cache within the processor package
  Improves performance
Memory controller
  Included in processor package
  Significant increase in system performance

## Slide 12: How a Processor Works
Figure 4-6 Quad-core processing with L1, L2, and L3 cache and the memory
controller within the processor housing
Notes: How a Processor Works

## Slide 13: Intel Processors
Table 4-1 Current Intel processors (continues)
Notes: Intel Processors

## Slide 14: Intel Processors
Table 4-1 Current Intel processors (continued)
Notes: Intel Processors

## Slide 15: Intel Processors
Processor identification
  Processor number
    Example: two Core i7 processors are identified as:
      i7-940 and i7-920
Centrino technology improves laptop performance
  Processor, chipset, wireless network adapter are interconnected as a unit
Intel Atom processor
  Low-powered processor
  Used in low-cost desktops, laptops, and netbooks
Notes: Intel Processors
Processor identification
  Processor number
    Example: two Core i7 processors are identified as:
      i7-940 and i7-920
Centrino technology improves laptop performance
  Processor, chipset, wireless network adapter are interconnected as a unit
Intel Atom processor
  Low-powered processor
  Used in low-cost desktops, laptops, and netbooks

## Slide 16: AMD Processors
Table 4-2 Current AMD processors (continues)
Notes: AMD Processors

## Slide 17: AMD Processors
Table 4-2 Current AMD processors (continued)
Notes: AMD Processors

## Slide 18: Selecting and Installing a Processor
PC repair technician tasks
  Assemble a PC from parts
  Exchange a faulty processor
  Add a processor
  Upgrade an existing processor
Must know how to:
  Match processor to system
  Install processor on motherboard
Notes: Selecting and Installing a Processor
PC repair technician tasks
  Assemble a PC from parts
  Exchange a faulty processor
  Add a processor
  Upgrade an existing processor
Must know how to:
  Match processor to system
  Install processor on motherboard

## Slide 19: Select a Processor to Match System Needs
First requirement
  Select a processor that the motherboard is designed to support
Select the best processor meeting general system requirements and user needs
  May have to sacrifice performance for cost
Notes: Select a Processor to Match System Needs
First requirement
  Select a processor that the motherboard is designed to support
Select the best processor meeting general system requirements and user needs
  May have to sacrifice performance for cost

## Slide 20: Install a Processor
Installing an Intel processor in Intel LGA socket (LGA 1150)
  1. Read motherboard user guide and follow directions
  2. Use an ESD strap or antistatic gloves
  3. Remove the socket protective cover
  4. Open the socket by pushing down on socket lever and gently push away from socket to lift lever
  5. Remove protective cover from processor
  6. Hold processor with index finger and thumb and align processor so the two notches on the edge of the processor line up with the posts embedded on the socket
Notes: Install a Processor
Installing an Intel processor in socket LGA1150
  1. Read motherboard user guide and follow directions
  2. Use an ESD strap or antistatic gloves
  3. Remove the socket protective cover
  4. Open the socket by pushing down on socket lever and gently push away from socket to lift lever
  5. Remove protective cover from processor
  6. Hold processor with index finger and thumb and align processor so the two notches on the edge of the processor line up with the posts embedded on the socket

## Slide 21: Install a Processor
Installing an Intel processor in Intel LGA socket (cont’d):
  7. Ensure the processor is aligned correctly in socket
  8. Return lever to its locked position
Notes: Install a Processor
Installing an Intel processor in socket LGA1150 (cont’d):
  7. Ensure the processor is aligned correctly in socket
  8. Return lever to its locked position

## Slide 22: Install a Processor
Figure 4-14 Orient the processor so the notches line up with the posts on the socket
Notes: Install a Processor

## Slide 23: Install a Processor
General steps to install a cooler
  1. Understand how cooler posts work
  2. Apply thermal compound if necessary (may be preapplied)
  3. Verify locking pins are turned counter-clockwise as far as they will go
  4. Push down on each locking pin until it pops into the hole
  5. Connect power cord from cooler fan to motherboard
  Check BIOS/UEFI setup to verify the system recognized processor after system up and running
Notes: Install a Processor
General steps to install a cooler
  1. Understand how cooler posts work
  2. Apply thermal compound if necessary (may be preapplied)
  3. Verify locking pins are turned counter-clockwise as far as they will go
  4. Push down on each locking pin until it pops into the hole
  5. Connect power cord from cooler fan to motherboard
  Check BIOS/UEFI setup to verify the system recognized processor after system up and running

## Slide 24: Install a Processor
Figure 4-17 Connect the cooler fan power cord to the motherboard CPU fan header
Notes: Install a Processor

## Slide 25: Install a Processor
Figure 4-26 A Pentium, cooler, and open socket 775
Notes: Install a Processor

## Slide 26: Install a Processor
Installing an AMD processor in an AMD socket (AM2+)
  Summary of installation steps
    1. Open the socket lever and remove protective cover
    2. Place processor in the socket
    3. Verify processor pins sitting slightly into the holes
    4. Press the lever down and gently into position
    5. Apply thermal compound and install cooler
    6. Clip into place the clipping mechanism on one side of the cooler
    7. Connect fan power cord to power connection
  Verify system works
Notes: Install a Processor
Installing an AMD processor in socket AM2+
  Summary of installation steps
    1. Open the socket lever and remove protective cover
    2. Place processor in the socket
    3. Verify processor pins sitting slightly into the holes
    4. Press the lever down and gently into position
    5. Apply thermal compound and install cooler
    6. Clip into place the clipping mechanism on one side of the cooler
    7. Connect fan power cord to power connection
  Verify system works

## Slide 27: Replacing the Processor in a Laptop
Before replacing, consider the laptop might still be under warranty or it might be more cost effective to replace the laptop rather than replacing processor
If decide to replace:
  Use CPU supported by manufacturer and notebook model
  For many laptops, remove the cover on the bottom to expose the processor fan and heat sink assembly
  Some laptops may require you to remove the keyboard and keyboard bezel to reach the fan assembly and processor
Notes: Replacing the Processor in a Laptop
Before replacing, consider the laptop might still be under warranty or it might be more cost effective to replace the laptop rather than replacing processor
If decide to replace:
  Use CPU supported by manufacturer and notebook model
  For many laptops, remove the cover on the bottom to expose the processor fan and heat sink assembly
  Some laptops may require you to remove the keyboard and keyboard bezel to reach the fan assembly and processor

## Slide 28: Replacing the Processor in a Laptop
If decide to replace (cont’d):
  Lift the CPU from the socket
    Lift straight up, without bending the CPU pins
  Before placing the new processor into the socket
    Be sure the socket screw is in the open position
  Place the processor into its socket
  Use thermal compound on top of the processor
Notes: Replacing the Processor in a Laptop
If decide to replace (cont’d):
  Lift the CPU from the socket
    Lift straight up, without bending the CPU pins
  Before placing the new processor into the socket
    Be sure the socket screw is in the open position
  Place the processor into its socket
  Use thermal compound on top of the processor

## Slide 29: Memory Technologies
Random access memory (RAM)
  Holds data and instructions used by CPU
  Dynamic RAM (DRAM)
    Memory modules used on a motherboard
Figure 4-36 RAM on motherboards today is stored in DIMMs
Notes: Memory Technologies
Random access memory (RAM)
  Holds data and instructions used by CPU
  Dynamic RAM (DRAM)
    Memory modules used on a motherboard

## Slide 30: Memory Technologies
Variations of DRAM
  DIMM – dual inline memory module
  small outline DIMM (SO-DIMM) – used on laptops
  microDIMMs – used on subnotebook computers
  RIMM - rambus inline memory module
  SIMM - single inline memory module
  RIMM and SIMM (outdated)
Differences among variations of DRAM:
  Data path width each module accommodates
  How data moves from system bus to module
Notes: Memory Technologies
Variations of DRAM
  DIMM – dual inline memory module
  small outline DIMM (SO-DIMM) – used on laptops
  microDIMMs – used on subnotebook computers
  RIMM and SIMM (outdated)
Differences among variations of DRAM:
  Data path width each module accommodates
  How data moves from system bus to module

## Slide 31: Memory Technologies
Table 4-3 Types of memory modules
Notes: Memory Technologies

## Slide 32: DIMM Technologies
DIMM (dual inline memory module)
  64-bit data path
  Independent pins on opposite sides of module
  Older DIMMs
    Asynchronous with system bus
  Synchronous DRAM (SDRAM)
    Runs synchronously with system bus
    Two notches
    Uses 168 pins
Notes: DIMM Technologies
DIMM (dual inline memory module)
  64-bit data path
  Independent pins on opposite sides of module
  Older DIMMs
    Asynchronous with system bus
  Synchronous DRAM (SDRAM)
    Runs synchronously with system bus
    Two notches
    Uses 168 pins

## Slide 33: DIMM Technologies
Double Data Rate SDRAM
  Also called DDR SDRAM, SDRAM II, DDR
    Two times faster than SDRAM and uses 184 pins
  DDR2 SDRAM
    Faster than DDR and uses less power
  DDR3 SDRAM
    Faster than DDR2 and uses less power
  DDR2 and DDR3
    Use 240 pins
    Not compatible: use different notches
  DDR4 – faster and uses less power than DDR3
    Uses 288 pins
Notes: DIMM Technologies
Double Data Rate SDRAM
  Also called DDR SDRAM, SDRAM II, DDR
    Two times faster than SDRAM and uses 184 pins
  DDR2 SDRAM
    Faster than DDR and uses less power
  DDR3 SDRAM
    Faster than DDR2 and uses less power
  DDR2 and DDR3
    Use 240 pins
    Not compatible: use different notches
  DDR4 – faster and uses less power than DDR3
    Uses 288 pins

## Slide 34: DIMM Technologies
Factors that affect capacity, features, and performance of DIMMS:
  Number of channels they use
  How much RAM is on one DIMM
  Speed
  Error-checking abilities
  Buffering
Notes: DIMM Technologies
Factors that affect capacity, features, and performance of DIMMS:
  Number of channels they use
  How much RAM is on one DIMM
  Speed
  Error-checking abilities
  Buffering

## Slide 35: DIMM Technologies
Early single channel DIMMs
  Memory controller is accessed one DIMM at a time
Dual channels
  Memory controller communicates with two DIMMs at the same time and doubles memory access speed
Triple channels
  Accesses three DIMMs at once
DDR, DDR2, DDR3, and DDR4 DIMMs use dual channels
  DDR3 DIMMs can also use triple channels
  DDR3 and DDR4 can use quad channels
Notes: DIMM Technologies
Early single channel DIMMs
  Memory controller is accessed one DIMM at a time
Dual channels
  Memory controller communicates with two DIMMs at the same time and doubles memory access speed
Triple channels
  Accesses three DIMMs at once
DDR, DDR2, DDR3, and DDR4 DIMMs use dual channels
  DDR3 DIMMs can also use triple channels
  DDR3 and DDR4 can use quad channels

## Slide 36: DIMM Technologies
Quad channeling
  Introduced with Intel Sandy Bridge chipsets and processors
  Processor can access four DIMMs at a time
Figure 4-41 The Intel Desktop Board DX79T0 has eight memory slots and supports two quad channels
Notes: DIMM Technologies
Quad channeling
  Introduced with Intel Sandy Bridge chipsets and processors
  Processor can access four DIMMs at a time

## Slide 37: DIMM Technologies
Setting up dual channeling
  Pair of DIMMs in a channel must be equally matched
    Size, speed, features
    Use same manufacturer (recommendation)
Figure 4-39 Matching pairs of DIMMs installed in four DIMM slots that support dual channeling
Notes: DIMM Technologies
Setting up dual channeling
  Pair of DIMMs in a channel must be equally matched
    Size, speed, features
    Use same manufacturer (recommendation)

## Slide 38: DIMM Technologies
Setting up triple-channeling
  Three DIMM slots populated with three matching DDR3 DIMMs
Figure 4-40 Three identical DDR3 DIMMs installed in a triple-channel configuration
Notes: DIMM Technologies
Setting up triple-channeling
  Three DIMM slots populated with three matching DDR3 DIMMs

## Slide 39: DIMM Technologies
DIMM Speed
  Measured in MHz and PC rating
PC rating
  Total bandwidth between module and CPU
  DDR2 PC rating
    Usually labeled PC2
  DDR3 PC rating
    Usually labeled PC3
  DDR4 PC rating
    Usually labeled PC4
Notes: DIMM Technologies
DIMM Speed
  Measured in MHz and PC rating
PC rating
  Total bandwidth between module and CPU
  DDR2 PC rating
    Usually labeled PC2
  DDR3 PC rating
    Usually labeled PC3
  DDR4 PC rating
    Usually labeled PC4

## Slide 40: DIMM Technologies
Single-sided DIMM
  Memory chips installed on one side of module
Double-sided DIMM
  Memory chips installed on both sides of module
Memory bank
  Memory a processor addresses at one time
  64 bits wide
Notes: DIMM Technologies
Single-sided DIMM
  Memory chips installed on one side of module
Double-sided DIMM
  Memory chips installed on both sides of module
Memory bank
  Memory a processor addresses at one time
  64 bits wide
Dual ranked
  DIMMs providing two or more banks
    Reduces overall memory price at the expense of performance

## Slide 41: DIMM Technologies
Error-correcting code (ECC)
  Detects and corrects error in a single bit
  Application: ECC makes 64-bit DIMM a 72-bit module
Parity – used by older SIMMs
  Error-checking based on an extra (ninth) bit
  Odd parity
    Parity bit set to make odd number of ones
  Even parity
    Parity bit set to make even number of ones
Parity error
  Number of bits conflicts with parity used
Notes: DIMM Technologies
Error-correcting code (ECC)
  Detects and corrects error in a single bit
  Application: ECC makes 64-bit DIMM a 72-bit module
Parity – used by older SIMMs
  Error-checking based on an extra (ninth) bit
  Odd parity
    Parity bit set to make odd number of ones
  Even parity
    Parity bit set to make even number of ones
Parity error
  Number of bits conflicts with parity used

## Slide 42: Types of Memory Used in Laptops
Today’s laptops use DDR, DDR3L, DDR3, or DDR2 SO-DIMM memory
Only use the type of memory the laptop is designed to support
The number of pins and the position of the notches on a SO-DIMM keep you from inserting the wrong module in a memory slot
Notes: Types of Memory Used in Laptops
Today’s laptops use DDR, DDR3L, DDR3, or DDR2 SO-DIMM memory
Only use the type of memory the laptop is designed to support
The number of pins and the position of the notches on a SO-DIMM keep you from inserting the wrong module in a memory slot

## Slide 43: How to Upgrade Memory
To upgrade memory means to add more RAM to a computer
Adding more RAM might solve:
  Slow performance
  Applications refusing to load
  An unstable system
  Windows “Insufficient memory” error message
Notes: How to Upgrade Memory
To upgrade memory means to add more RAM to a computer
Adding more RAM might solve:
  Slow performance
  Applications refusing to load
  An unstable system
  Windows “Insufficient memory” error message

## Slide 44: How to Upgrade Memory
Questions to ask
  How much RAM do I need and how much is currently installed?
  How many and what kind of memory modules are currently installed on my motherboard?
  How many and what kind of modules can I fit on my motherboard?
  How do I select and purchase the right modules for my upgrade?
  How do I physically install the new modules?
Notes: How to Upgrade Memory
Questions to ask
  How much RAM do I need and how much is currently installed?
  How many and what kind of memory modules are currently installed on my motherboard?
  How many and what kind of modules can I fit on my motherboard?
  How do I select and purchase the right modules for my upgrade?
  How do I physically install the new modules?

## Slide 45: How Much Memory Do I Need and How Much Is Currently Installed?
Best answer: “All you can get”
  Windows 10 require at least 4 GB RAM
    But more is better
  32-bit installation of Windows 10
    4 GB installed RAM
  64-bit installation of Windows 10
    More than 4 GB installed RAM
Notes: How Much Memory Do I Need and How Much Is Currently Installed?
Best answer: “All you can get”
  Windows 8/7 require at least 2 GB RAM
    But more is better
  RAM limit for a 32-bit OS
    4 GB installed RAM
  64-bit installation of Windows 8
    Can use up to 128 GB of RAM
  64-bit installation of Windows 7 Home Premium
    Can use up to 16 GB of RAM

## Slide 46: How Many and What Kind of Modules Are Currently Installed?
Open the case and look at memory slots
  How many slots?
  How many filled?
  Review module imprint
Examine module for physical size and notch position
Read motherboard documentation
  See if board supports dual, triple, or quad channels
Last resort
  Take motherboard and old memory modules to a good computer parts store for confirmation
Notes: How Many and What Kind of Modules Are Currently Installed?
Open the case and look at memory slots
  How many slots?
  How many filled?
  Review module imprint
Examine module for physical size and notch position
Read motherboard documentation
  See if board supports dual, triple, or quad channels
Last resort
  Take motherboard and old memory modules to a good computer parts store for confirmation

## Slide 47: How Many and What Kind of Modules Can Fit on My Motherboard?
Read motherboard documentation
  Indicates how much memory motherboard can physically hold
DIMM modules
  DIMMs can be installed as single modules
  Motherboard supporting dual channeling
    Install matching DIMMs in each channel for best performance
  DDR3 board supporting triple channeling
    For best performance install three matching DIMMs in triple-channel slots
Notes: How Many and What Kind of Modules Can Fit on My Motherboard?
Read motherboard documentation
  Indicates how much memory motherboard can physically hold
DIMM modules
  DIMMs can be installed as single modules
  Motherboard supporting dual channeling
    Install matching DIMMs in each channel for best performance
  DDR3 board supporting triple channeling
    For best performance install three matching DIMMs in triple-channel slots

## Slide 48: How Many and What Kind of Modules Can Fit on My Motherboard?
Motherboard using DDR DIMMs with dual channeling
  Allows three different DDR DIMM speeds in one to four sockets, supports dual channeling
  Two blue memory slots and two black slots
  For dual channeling
      Matching DIMMs must be installed in the two blue sockets
  If two DIMMs installed in the two black sockets
      They must match each other
Notes: How Many and What Kind of Modules Can Fit on My Motherboard?
Motherboard using DDR DIMMs with dual channeling
  Allows three different DDR DIMM speeds in one to four sockets, supports dual channeling
  Two blue memory slots and two black slots
  For dual channeling
      Matching DIMMs must be installed in the two blue sockets
  If two DIMMs installed in the two black sockets
      They must match each other

## Slide 49: How Do I Select and Purchase the Right Memory Modules?
Compromises if the exact match is not available:
  Mixing unbuffered memory with buffered or registered memory will not work
  Match memory module manufacturer, if possible
    In a pinch, try using memory from two different manufacturers
  If mixing memory speeds:
    All modules perform at slowest speed
Notes: How Do I Select and Purchase the Right Memory Modules?
Compromises if the exact match is not available:
  Mixing unbuffered memory with buffered or registered memory will not work
  Match memory module manufacturer, if possible
    In a pinch, try using memory from two different manufacturers
  If mixing memory speeds:
    All modules perform at slowest speed

## Slide 50: How Do I Select and Purchase the Right Memory Modules?
Using a web site to research your purchase
  Look for search utility matching modules to board
Figure 4-52 The Kingston web site DIMM recommendations for a particular motherboard
Notes: How Do I Select and Purchase the Right Memory Modules?
Using a web site to research your purchase
  Look for search utility matching modules to board

## Slide 51: How Do I Install the New Modules?
Precautions:
  Always use an ESD strap
  Turn off power, unplug power cord, press power button, remove case cover
  Handle memory modules with care
  Do not touch edge connectors on memory module or memory slot
  Do not stack cards or modules
  Look for notches on one side or in the middle for correct orientation
Notes: How Do I Install the New Modules?
Precautions:
  Always use an ESD strap
  Turn off power, unplug power cord, press power button, remove case cover
  Handle memory modules with care
  Do not touch edge connectors on memory module or memory slot
  Do not stack cards or modules
  Look for notches on one side or in the middle for correct orientation

## Slide 52: How Do I Install the New Modules?
Installing DIMMS
  Pull out supporting arms on the sides of the slot
  Use notches on DIMM edge connector as a guide
  Insert DIMM straight down into the slot
  Ensure supporting arms lock into position
New installations are generally uncomplicated
  Usually involve placing memory on motherboard
  Older computers may need change to BIOS setup
  If new memory not recognized try reseating the module
Notes: How Do I Install the New Modules?
Installing DIMMS
  Pull out supporting arms on the sides of the slot
  Use notches on DIMM edge connector as a guide
  Insert DIMM straight down into the slot
  Ensure supporting arms lock into position
New installations are generally uncomplicated
  Usually involve placing memory on motherboard
  Older computers may need change to BIOS setup
  If new memory not recognized try reseating the module

## Slide 53: How to Upgrade Memory on a Laptop
Upgrade process is similar to desktops
  Considerations:
    Make sure warranty not being voided
    Search for best buy on a suitable and authorized part
  General steps:
    Decide how much memory to upgrade
    Purchase memory
    Install it
  Be sure to match the type of memory to the type the laptop supports
Notes: How to Upgrade Memory on a Laptop
Upgrade process is similar to desktops
  Considerations:
    Make sure warranty not being voided
    Search for best buy on a suitable and authorized part
  General steps:
    Decide how much memory to upgrade
    Purchase memory
    Install it
  Be sure to match the type of memory to the type the laptop supports

## Slide 54: Summary
Processor: most important motherboard component
  Two major manufacturers are Intel and AMD
Processors are rated by speed of the system bus, the socket and chipset, processor architecture, multi-core rating, internal memory cache, amount and type of RAM and computing technologies
Memory cache inside the processor housing can be L1, L2, and L3 cache
Core of processor has two arithmetic logic units (ALUs) and each core can process two threads at once
Notes: Summary
Processor: most important motherboard component
  Two major manufacturers are Intel and AMD
Processors are rated by speed of the system bus, the socket and chipset, processor architecture, multi-core rating, internal memory cache, amount and type of RAM and computing technologies
Memory cache inside the processor housing can be L1, L2, and L3 cache
Core of processor has two arithmetic logic units (ALUs) and each core can process two threads at once

## Slide 55: Summary
Current families of Intel processors include Core, Atom, Celeron, and Pentium
Current AMD processor families include FX, Phenom, Athlon, and Sempron
Select a processor that the motherboard supports
When installing, always follow directions in motherboard user guide
DRAM is stored on DIMMs for desktops and SO-DIMMs for laptops
DIMMs can be single-sided or double-sided
Notes: Summary
Current families of Intel processors include Core, Atom, Celeron, and Pentium
Current AMD processor families include FX, Phenom, Athlon, and Sempron
Select a processor that the motherboard supports
When installing, always follow directions in motherboard user guide
DRAM is stored on DIMMs for desktops and SO-DIMMs for laptops
DIMMs can be single-sided or double-sided

## Slide 56: Summary
DIMMs can work together in dual, triple, or quad channels
DIMM speeds are measured in MHz or PC rating
The memory controller can check memory for errors and possibly correct those errors using ECC
Buffers and registers are used to hold data and amplify a data signal
CAS Latency and RAS Latency measure access time to memory
When upgrading memory, use the type, size, and speed the motherboard supports
Notes: Summary
DIMMs can work together in dual, triple, or quad channels
DIMM speeds are measured in MHz or PC rating
The memory controller can check memory for errors and possibly correct those errors using ECC
Buffers and registers are used to hold data and amplify a data signal
CAS Latency and RAS Latency measure access time to memory
When upgrading memory, use the type, size, and speed the motherboard supports